## Slide 1: Real-Time Biomechanical Tracking Framework
Integrating Movella DOT Sensors with OpenSim SDK on Windows 11
Presenter: Srushti

## Slide 2: The Engineering Challenge
Objective: Stream dual-arm data for joint angle estimation.
The Roadblock: Custom Python scripts returned 0 Hz streams.
OS Restrictions: Windows 11 aggressively filtered third-party BLE packets.
Handshake Security: Newer Movella firmware ignores unauthenticated BLE requests.

## Slide 3: Root Cause Analysis & Pivots
Mac vs Windows: Medium blog patterns failed on Windows architecture.
Firmware v2 Shifts: Custom UUID streams required explicit descriptor triggers.
The Solution: Transitioned from raw Bleak code to official SDK bindings.
Environment Alignment: Resolved Python version mismatches via custom wheel packaging.

## Slide 4: System Integration Architecture
IDE Workspace: Consolidated editing and execution within VS Code.
Thread Safety: Implemented asyncio Queue arrays for background streams.
C++ Backend: Loaded native Movella binary hooks via xdpchandler.py.
Hardware Isolation: Filtered out ambient environmental sensors using address whitelists.

## Slide 5: Bridging to OpenSim SDK
GUI Limitations: Bypassed frozen OpenSim desktop user interface configurations.
C++ Binary Paths: Resolved simbody DLL lookup failures via runtime injection.
Graphics Workaround: Disabled OpenGL visualization to prevent driver crashes.
Biomechanical Mapping: Synchronized tracking streams to the native r_elbow_flex coordinate.

## Slide 6: Final Milestones & Success
Antenna Stability: Sustained flawless multi-sensor connection streams.
Live IK Calculation: Extracted real-time joint degree modifications at 60 Hz.
Clean Fallbacks: Implemented thread-safe hardware socket closure.
Next Steps: Exporting real-time kinematic arrays to motion trajectory logs.